A3

IEA Large Tokamak Cooperation

REPORT FORM to Secretariat (Workshop)		                                   (Form C)

Workshop Number:	W64

Subject:	IEA Large Tokamak IA Workshop on

“Edge Transport in Fusion Plasmas”

Date:	11-13 September 2006

Place:	Dom Polonii, Kraków, Poland

Name (s) of attendees:          (All names of attendees are listed in the attachment.)

Brief description of the activities in the Workshop W64

The workshop was held in Krakow, Poland from the 11th to 13th of September 2006, in the cultural center “Dom Polonii”. A detailed list of the 30 participants is provided in the appendix, along with agenda of the workshop. The first day (Monday) focused on edge turbulence with experimental results being reported in the morning session and theoretical work in the afternoon session. The second day (Tuesday) was similarly divided (morning – experiment, afternoon - experiment) with the topic being edge localized modes or ELMs. The final day (Wednesday) contained a morning session dedicated to challenges in edge modeling with fluid codes, and an afternoon session including a plenary discussion followed by smaller working group discussions. The outline of each session is presented below.

In the Monday morning session (chaired by W.Fundamenski), S.Zweben presented a comprehensive overview on recent observations of edge turbulence with fast cameras, pointing out that turbulent structures in the edge are a sincere issue for ITER. Besides results he also reviewed available diagnostic methods for the edge and the emerging comparison with detailed turbulence calculations. J.Horacek reported on results from TCV on detailed investigations using probes of edge and SOL properties with good comparison to ESEL modeling. M.Hron showed recent results from the Czech tokamak CASTOR including biasing experiments in the SOL leading to improved confinement. The stochasticity in magnetic field lines at the ergodic divertor at TEXTOR  and its impact heta and particle deposition was the topic of a talk by M.Jakubowski, depicting the relevance of the length of the ergodic field lines for heat deposition and the question of stochastic transport vs. collisional transport.  First results and the construction on the FTU liquid Lithium limiter including observations of high density peaking at reduced Zeff  were presented by V. Pericoli-Ridolfini. P. Scarin reported on structures in the edge turbulence on RFX showing scalings in the structures and the spectra with density.

The Monday afternoon session (chaired by V.Naulin) dealt with theoretical progress made in edge turbulence simulations. B.Scott presented an overview of recent developments in edge turbulence codes and the requirements for energy transfer terms required for realistic numerical simulations. A.Kendl reported on the influence of magnetic field geometry on the turbulence, while T.Ribeiro presented first calculations showing the change of the turbulence characteristic from the drift wave type on closed magnetic field lines to interchange type on open field lines. T.S.Hahm showed the importance of turbulence spreading from the edge into the core and in general into stable regions. A.Nielsen presented ESEL simulations for JET showing fair agreement in predicting e-folding length and radial transport profiles, while stressing that corresponding ITER simulations will see a tenfold increase in computational resources.

In the Tuesday morning session (chaired by W.Fundamenski), K.Kamiya presented an overview of experimental observations of edge localized models (ELMs) in present day large tokamaks, including recent results on the effect of toroidal field ripple (varied with ferromagnetic insets) on ELM size on JT-60U. Peter Balan showed recent measurements for Reynolds stress and particle fluxes in the quiescent inter-ELM phasesand compared these with numerical simulations of 2D SOL interchange turbulence for ASDEX Upgrade parameters. K.H.Finken reported on the Influence of the Dynamic Ergodic Divertor (DED) in the Textor tokamak on ELM behaviour, including the suppression of ELM activity at even moderate DED currents. S.Zweben, reporting for R.J.Maqueda who could not attend for personal reasons, showed High Speed Images of Edge Plasmas in NSTX; the images revealed an apparent continuum in intermittent activity and phenomenology of filamentary structures from ohmic through L-mode to ELMy H-mode conditions. E.Nardon discussed the simulations of ELM control by resonant magnetic perturbations (RMP) for ITER, including the expected response of the plasma to the RMP as predicted by the non-ideal MHD code JOREK. The screening of the RMP due to toroidal rotation was suggested to explain the fall of the edge density with RMP in the DIII-D I-coil experiments. In the final talk, G.Kirnev reported on Investigation of nonlinear interactions of plasma fluctuations in the edge of the T-10 tokamak, showing a two wave decomposition of the observed fluctuatios into several pairs of the frequency components (with frequencies f1 and f2) obeying the rule f1+f2 = f0.

The Tuesday afternoon session (chaired by T.Rognlien) dealt with progress in the theory and simulations of ELMs. G. Huysmans presented an overview talk in which he described several approaches at modeling the ELM. Non-ideal MHD codes were shown to be fairly successful in modeling the early non-linear phase of the ELM evolution. X-point geometry and plasma dissipative effects were shown to be important in this context. O.E.Garcia presented dynamical simulations of  isolated blobs and ELM  filaments in SOL plasmas based on electrostatic interchange dynamics. He showed that It is demonstrated that such plasma filaments develop dipolar vorticity and electrostatic potential fields, resulting in rapid radial acceleration and formation of a steep front and a trailing wake. A.H.Kritz discussed the Modeling of ELM Dynamics in ITER. He addressed the important question of integrated modeling of ELMy H-mode discharges, namely how much plasma and current density is removed during each ELM crash. Non-ideal MHD simulations using the NIMROD code indicate the formation of ELM filament structures, which are observed in many existing tokamak experiments, in marginally stable ITER equilibria. Differences between ELM dynamics for ELMs triggered by ballooning instabilities and by peeling instabilities are described. M.Tokar discussed modeling of mechanisms responsible for ELM mitigation by external magnetic field perturbations. He demonstrated that through non-linear interaction, leading to the generation of side bands which suck energy from the main mode, such perturbations can raise the threshold of MHD instabilities. D.Kalupin presented simulations of the effect of pulsed gas puffing as a trigger for the ETB formation, using the 1-D transport code RITM. The results indicate that the turbulent transport is transiently suppressed by the shear of the radial electrical field, which emerges at the plasma edge due to the formation of the steep pressure gradient driven by the gas injection. Finally, P.Belo discussed the effect of the edge transport barrier on impurity transport using the 2D transport code EDGE2D. She found that the decrease in the deuterium puff level lead to an increase in the parallel classical thermal force, such that the sum of the parallel friction and thermal forces was directed away from the divertor region allowing impurities to concentrate in the plasma core.

In the Wednesday morning session (chaired by V.Naulin), was devoted to numerical approaches to edge modeling. R. Schneider presented an overview on current challenges in edge modeling pointing out the successes in edge modeling over the last decade, but also lasting complex questions that need addressing in an integrated way. He showed the scope of edge modeling from molecular dynamics simulations  via kinetic and gyrokinetic calculations to the more ubiquitous fluid models. He also called for integrated modeling as is happening in other engineering and physics fields with well defined measures for quality assessment and code integration. C.S. Chang presented the SciDAC program on integrated simulation of edge transport in fusion plasmas and showed first results from the full f gyrokinetic  XGC-1 PIC code. He called for an integrated approach to turbulence and neoclassic in the edge as conventional neoclassical theory often breaks down for the SOL. Coupling of the code to an MHD code is underway. T. Rognlien presented the  progress on a continuum gyrokinetic code for edge plasmas and results from early physics benchmarks from modules of the code. . H. Kawashima reported on JT60U/JT-60SA simulations and development of a integrated SOL/divertor code in JAEA. An effort to integrate particle and fluid codes for the edge is underway. Results on sputtering and divertor pumping were presented. . Kalentiev presented results from different numerical approaches to 3D transport modeling of fusion devices, focusing on three competitive codes under development for W7-X . One problem being the mapping of a complex, evolving magnetic field structure to a usable and computational beneficial numerical grid.  J. Brooks considered sputtered  impurity edge plasma transport modeling for ITER parameters and the spatial distribution of sputtered material from the ITER wall. Large uncertainties in the material redeposition properties were reported.

The concluding discussion session on Wednesday afternoon was chaired by W. Fundamenski, V. Naulin and R. Zagorski. Topics of the previous days were taken up in a vivid discussion on the convergence of large scale MHD models towards fluid turbulence models. The need for better benchmarking of codes was stressed as the need for development and maintenance of larger code projects. It was agreed that some progress will be made on the inclusion of atomic physics into transport codes and the coupling of these to turbulence codes. The experimental side has benefited from better diagnostics in the edge, with a clear call for improved spatiotemporal diagnostics and quantification of fast camera data.

=============================================================

This report received by Secretariat on    day   mo     y

N

Agenda

Monday

| Time | Speaker | Title |
| --- | --- | --- |
| 09.00-12.30 |  | Session 1: Edge Turbulence - Experiment Chaired by W. Fundamenski |
| 09.00 | S. Zweben | Edge plasma turbulence: experiment |
| 09.40 | J. Horacek | Understanding SOL plasma turbulence by interchange motions |
|  | M. Hron | Edge plasma studies on the CASTOR tokamak |
| 10.25 |  | Coffee break |
| 10.50 | M. Jakubowski | The role of the stochastic and laminar field lines on the |
|  |  | heat and particle deposition patterns of the ergodic divertor on TEXTOR |
|  | V. Pericoli-Ridolfini P. Scarin | Modification of the SOL properties with the liquid lithium limiter in FTU- experiment and transport modeling Evidence of edge turbulence structure in RFX-mod virtual shell discharges with Gas Puffing Imaging Diagnostic |
| 12.00 |  | Discussion |
| 14.00-17.25 |  | Session 2: Edge Turbulence – Theory Chaired by V. Naulin |
| 14.00 | B. Scott | Turbulence theory |
| 14.40 | A. Kendl T. Ribeiro | Edge plasma turbulence theory: the role of magnetic topology Drift wave turbulence on closed and open flux surfaces: effect limiter / divertor plates location |
| 15.25 |  | Coffee break |
| 15.50 | T.S. Hahm A.H. Nielsen | Role of turbulence spreading in edge-core coupling Interchange turbulence simulations for JET for relevant parameters |
| 17.00-17.45 |  | Discussion |
| 19.00 | Conference Dinner |

Tuesday

| Time | Speaker | Title |
| --- | --- | --- |
| 09.00-12.30 |  | Session 3: ELMs - Experiment Chaired by W. Fundamenski |
| 09.00 | K. Kamiya | Edge localized modes: resent experimental findings and related issues |
| 09.40 | P. Balan K.H. Finken | Investigation of fluctuation in the SOL of ASDEX upgrade by Langmuir probes Influence of the dynamics ergodic divertor on ELM activities |
| 10.25 |  | Coffe ebreak |
| 10.50 | R.J. Maqueda (S.Zweben) E. Nardon G. Kirnev | High speed images of edge plasmas in NSTX and Alcator C-mod Edge localized modes control by resonant magnetic perturbations Investigation of nonlinear interactions of plasma fluctuations in the edge of the T-10 tokamak |
| 12.00 |  | Discussion |
| 14.00-17.25 |  | Session 4: ELMs: Theory Chaired by T. Rognlien |
| 14.00 | G. Huysmans | Edge localized modes: Theory |
| 14.40 | O.E. Garcia | Radial motion of isolated blobs and ELM filaments in |
|  | A.H. Kritz | SOL plasmas Modeling of ELM dynamics in ITER |
| 15.25 |  | Coffee break |
| 15.50 | M. Tokar D. Kalupin P. Belo | Modeling of mechanisms responsible for ELM mitigation by external field perturbations Pulsed gas puffing as a trigger for the ETB formation Effect of the edge transport barrier on impurity |
|  |  | transport |
| 17.00-17.45 |  | Discussion |

Wednesday

| Time | Speaker | Title |
| --- | --- | --- |
| 09.00-12.30 |  | Session 5: Edge Modelling Chaired by V. Naulin |
| 09.00 | R. Schneider | Challenges in edge modeling |
| 09.40 | C.S. Chang T. Rognlien | US SciDAC program on integrated simulation of edge transport in fusion plasmas, and its progress Progress on a continuum kinetic code for edge plasmas |
| 10.25 |  | Coffee break |
| 10.50 | H. Kawashima O. Kalentiev J. Brooks | Development of integrated SOL/divertor code and simulation study of theJT60U/JT-60SA tokamak Different numerical approaches to 3D transport modeling of fusion devices Modeling of sputtered impurity edge plasma transport-new directions and challenges |
| 12.00 |  | Discussion |
| 14.00-16.00 |  | Session 6: |
|  |  | General Discussion and future collaborations |
|  |  | (working groups) |
| 16.00 |  | End of Workshop |

LIST OF PARTICIPANTS

EU:	Balan Petru (Innsbruck University)

Belo Paula (CFN/IST Lisbon, Portugal)

Finken Karl Heinz (IPP, Forschungszentrum Juelich,Germany)

Fundamenski Wojtek (Euratom-UKAEA)

Garcia Odd Erik (Riso National Laboratory, Denmark)

Horacek Jan. (Institute of Plasma Physics, Czech Republic)

Hron Martin (Institute of Plasma Physics, Czech Republic)

Huysmans Guido (Association Euratom/CEA Cadarache, France) Jakubowski Marcin (IPP, Forschungszentrum Juelich,Germany)

Kalentiev Oleksander (IPP Greifswald, Germany)

Kalupin Denis (IPP, Forschungszentrum Juelich,Germany)

Kendl Alexander (University of Innsbruck)

Nardon Eric (Association Euratom/CEA Cadarache, France)

Naulin Volker (Riso National Laboratory, Denmark)

Nielsen Anders Henry (Riso National Laboratory, Denmark)

Pericoli-Ridolfini Vincenzo (ENEA - C.R.FRASCATI, Italy)

Ribeiro Tiago (IPP - Garching, EURATOM Association, Germany)

Scarin Paolo (Consorzio RFX, Enea-Euratom, Italy)

Schneider Ralf (IPP Greifswald, Germany)

Scott Bruce (IPP - Garching, EURATOM Association, Germany)

Tokar Mikhail (IPP, Forschungszentrum Juelich,Germany)

Zagórski Roman (EURATOM-IPPLM, Warsaw, Poland)

USA:	Brooks Jeffrey (Argonne National Laboratory,USA )

Chang Choong-Seoc (Courant Institute of Mathematical Sciences, New Jersey, USA)

Hahm Taik Soo (PPL, Princeton University, USA)

Rognlien Tom (Lawrence Livermore National Laboratory, USA)

Zweben Stewart (PPL, Princeton University)

JAPAN:  Kamiya Kensaku (Japan Atomic Energy Agency)

Kawashima Hisato (Japan Atomic Energy Agency)

RUSSIA: Kirnev Gennady (RRC, Kurchatov Institute, Moscow, Russia)

CHINA:  -

KOREA: -

IEA Large Tokamak Cooperation

REPORT FORM to Secretariat (Workshop)		                                   (Form C)

Workshop Number:	W65

Subject:	Fifth Joint workshop of Large Tokamak , Poloidal Divertor and Textor IA's on "Implementation of the ITPA Coordinated Research Recommendations"

Date:	Nov. 30 - Dec. 1, 2006

Place:	JAEA, Naka, Japan

Name (s) of attendees:          (All names of attendees are listed in the attachment.)

Brief description of the activities in the Workshop W65

The 5th annual Workshop for the planning of ITPA/IEA joint experiments to implement the ITPA high priority research tasks was held at JAEA Naka on November 30 and December 1.  About 33 participants (see Attachment #1) included Executive Committee members of the three tokamak related IEA IAs, Chairs, Co-Chairs, and some members of the ITPA Coordinating Committee and its Topical Groups, and Leaders or their representatives of ~ 14 tokamak programs in the seven ITER Parties (CN, EU, IN, JA, KO, RF, and US).  The previous workshops for the planning of Joint Experiments were held at MIT, USA (Nov 02), Naka, Japan (Dec. 03), and Oxford, UK (Dec. 04), General Atomics, USA (Nov. 05).

The meeting agenda is shown in Attachment 2.  F. Romanelli (EFDA) made opening comments as the Chair of the IEA LT ExCo. P.Gohil (GA), representing T. Taylor (GA), reported briefly on the 4th Workshop held at GA, USA in 2005.  Ron Stambaugh, Chair of the ITPA Coordinating Committee reported on the status of Joint Experiments that were planned at the last meeting. For preparation of the discussion on the joint experiments, the present status of the world tokamak devices were introduced by updating information on the new hardware capabilities, their operating schedules, and major topical areas of their research programs.

After the last meeting in 2005, 63 joint experiments were active. Among them, new results have been obtained in 34 experiments.

In this meeting, the seven ITPA Topical Groups proposed 11 new joint experiments and updated their proposed research on the experiments to be continued into 2007.  Thus there were 65 joint proposals for CY2007 for the participants to review and plan for CY 2007.  The TG Chairs or Co-Chairs provided one page summaries of these proposals, including the progress made previously, and their recommendations for tokamaks that should participate in these experiments to provide the parameter range for the experiments.

These presentations were then followed with comments by the tokamak leaders or their representatives considering their tokamak programs and schedules, and technical details and the necessary basis of proposed joint experiments .

The last session was dedicated to a brief review each proposal, receiving an expression of interest from the tokamak leaders to participate in the specific joint experiment, and to identify spoke-persons for the joint experiments and the names of the contact persons from the participating tokamaks.  This activity led to the development of the Joint Experiments Plan for FY 2007, which is shown in Attachment 3.  The commitments from some of the tokamaks are not yet firm (indicated in green), pending finalization of Research Forums of the individual programs and their process to finalize their experimental program plans.  Most tokamaks (in red) were committed to the experiments.  The tokamaks participating in the joint experiments, but completed their experimental runs earlier are shown in black.

The process of developing joint experiments has matured during these past four years, and most proposals were well defined and involved coordinated joint experiments.  These are labeled as ready for Experiments (E).  Some proposals, categorized as D, required additional discussions for joint experiments, partly because tokamak leaders expressed an interest to join the experiment at the meeting and their participation needed to be defined.  Only a few proposals were labeled as P, indicating that this is an ongoing programmatic activity, such as collecting database, with minimal coordination among the participating tokamaks.

=============================================================

This report received by Secretariat on    day   mo     y

Appendix 1:  Agenda

|  | AGENDA |  |
| --- | --- | --- |
| Nov. 30 , Thursday, 2006 |  |  |
| 08:30 | Welcome | M. Kikuchi |
| 08:40 | Logistics | S. Ide |
| 08:45 | Opening Remarks | F. Romanelli |
| 08:50 | Report from last Workshop | P. Gohil |
| 09:20 | Status of IEA/ITPA Joint Experiments (2006) | R. Stambaugh |
| 09:50 | BREAK |  |
| 10:05 | ITER Research Needs | D. Campbell / M.Shimada |
| 10:30 | Machine Status (5 minutes & 3 viewgraphs each) VG#1–New machine capabilities in CY07 - 08 VG#2–Operating Schedule in CY07 - 08 VG#3–Research Focus Areas in CY07 - 08 JET JT-60U DIII-D AUG C-Mod Tore Supra TEXTOR TCV FTU NSTX MAST Russian Tokamaks Chinese Tokamaks SST-1 Discussion | (Ch. S. Ide ) M. Watkins S. Ishida T. Taylor J. Schweinzer J. Rice J. Bucalossi D. Campbell J. Rice A. Tuccillo M. Peng B. Lloyd S. Konovalov B. Wan A. Sen |
| 12:00 | LUNCH (JAEA cafeteria) |  |
| 13:30 | Proposals for IEA/ITPA Joint Experiments (2007) 1. Transport Physics 2. Confinement Database and Modeling 3. Steady State Operation 4. Edge Physics and Pedestal 5. MHD 6. Divertor and SOL 7. Diagnostics | (Ch: P. Gohil) R. Stambaugh E. Doyle W. Houlberrg G. Sips H. Urano Y. Gribov N. Asakura A. Costley |
| 15:45 | BREAK Move to ITER Conference Room |  |
| 16:10 | Break-out session for Program Leaders 1. To discuss proposed list of Joint Experiments 2. To discuss identification and implementation of other experiments not on list of proposed experiments 3. To discuss level of prioritization or expectation of commitment by each device for the list of proposed joint experiments 4. Input to Stambaugh by end of the day |
| 17:30 | Workshop Adjourns |  |

| Dec. 1, Friday, 2006 |  |  |
| --- | --- | --- |
| 9:00 - 12:00 | Chair: M. Shimada Plenary Discussion of the Proposed Roster of Joint Experiments for 2007 | R. Stambaugh |
| 12:00 | LUNCH ((JAEA cafeteria) |  |
| 13:00 | Concluding Discussions | F. Romanelli |
| 14:20 | Concluding Remarks and Close of Meeting | F. Romanelli |
| 14:30 | END (nominal time) |  |

Appendix 2:  LIST OF PARTICIPANTS

| Name | Organization |
| --- | --- |
| Romanelli Francesco | EFDA |
| Pamela Jerome Hubert | EFDA |
| Campbell David John | EFDA |
| Watkins Michael Lewis | JET |
| Lloyd Brian | UKAEA |
| Schweinzer, Josef | Max Planck Institut fuer Plasmaphysik |
| Sips Adrianus Cornelis | Max Planck Institut fuer Plasmaphysik |
| Bucaloss Jerome | CEA-EURATOM |
| Tuccillo Angelo Antonio | ENEA |
| Samm Ulrich | Forschungszentrum Jülich GmbH, Institut für Plasmaphysik |
| Erol Oktay | U.S. Department of Energ |
| Houlberg Wayne Arthur | Oak Rigde National Laboratory |
| Peng Yueng-Kay Martin | Oak Rigde National Laboratory |
| Gohil Punit | General Atomics, USA |
| Taylor Tony S. | General Atomics, USA |
| Stambaugh Ronald | General Atomics, USA |
| Doyle Edward | University of California, Los Angels, USA |
| Rice John Edward | MIT PSFC, USA |
| Sen Abhijit | Institute for Plasma Research, India |
| Konovalov Sergey | Kurchatov Institute, RF |
| Wan Baonian | ASIPP, China |
| Myeun Kwon | National Fusion Research Center, Korea |
| Kikucji, Mitsuru | JAEA, Japan |
| Ishida, Shinichi | JAEA, Japan |
| Kamada, Yutaka | JAEA, Japan |
| Asakura, Nobuyuki | JAEA, Japan |
| Shinohara, Koji | JAEA, Japan |
| Urano, Hajime | JAEA, Japan |
| Shimada, Michiya | ITER |
| Grivov, Yuri | ITER |
| Mokhovatov, Vladimir | ITER |
| Costlay, Alan | ITER |
| Polevoi, Alexei | ITER |

Appendix 3: List of Joint Experiments for 2007

| ID No | Topical Group | Proposal Title | Keypersons 1 | Devices 2 | Ctg | Comments/ Recommendations/ Results |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Green = Spokesperson Underline = Machine representative in cases with more than one person from that machine. | Red = Committed, Green = Considering, Blue = Not doing in coming year Black = Completed | See bottom | Report = Report done for previoius year |
| CDB-1 | Conf DB & Mod | Effects of inside and vertical pellet launch | W A Houlberg and others | Black | P | Regarded as programmatic, see also CDB-5; Closed 2005 |
| CDB-2 | Conf DB & Mod | Confinement scaling in ELMy H-modes:  degradation | F Ryter, C C Petty, D. C. McDonald, T. Takizuka, F. Imbeaux/ T. Hoang(TS), M. Valovic(MAST), S. Kaye | AUG, DIII-D, JET, JT-60U, Tore-Supra(L), MAST, NSTX | E | Report, new results, related to PEP 20 and SSO-4 |
| CDB-3 | Conf DB & Mod | Improving the condition of Global ELMy H-mode and Pedestal databases | F Ryter, J DeBoo, J G Cordey | AUG, DIII-D, JET, JT-60U, C-Mod | E | Report; Closed 2005 |
| CDB-4 | Conf DB & Mod | Confinement scaling in ELMy H-modes: * scans at fixed n/nG | J Snipes, C C Petty, H. Leggate, J. Stober | C-Mod, DIII-D, JET, AUG | E | Report, defer to 07 |
| CDB-5 | Conf DB & Mod | Effects of inside and vertical pellet launch: ELM behaviour | P Lang, L Baylor, G Saibene, A Loarte | AUG, DIII-D, JET, HT-7, JT-60U, MAST, HL-2A | P | Report; Closed 2005 |
| CDB-6 | Conf DB & Mod | Improving the condition of Global ELMy H-mode and Pedestal databases: Low A | S Kaye, M. Valovic, C. Petty | MAST, NSTX, DIII-D | E | Report, new results |
| CDB-7 | Conf DB & Mod | Ohmic Identity Experiments: test of scaling with dimensionless parameters | F Ryter, M Romanelli, J G Cordey, H Weisen, F Imbeaux | AUG, FTU, JET, TCV, Tore Supra, HL-2A, C-MOD | E | Report, Accept recommendation to abandon project; Closed 2005 |
| CDB-8 | Conf DB & Mod | * scaling along an ITER relevant path at both high and low beta | D.C. McDonald, C. Petty, M. Greenwald, S.Kaye, A. Staebler | JET, DIII-D, C-mod, AUG, NSTX | E | Report, preparation for 07 |
| CDB-9 | Conf DB & Mod | Density profiles at low collisionality | H. Weisen(JET), M. Valovic(JET), T. Casper(DIII-D),M. Greenwald (C-mod), C. Angioni(AUG), H. Takenaga(JT-60U), H. Weisen/O. Sauter(TCV), T. Hoang(Tore-Supra), M. Valovic(MAST) | JET, DIII-D, C-mod, AUG, JT-60U, TCV, Tore-Supra, MAST,NSTX | D | Report, analysis of previous data, experiment deferred to 07. Experiment proposal need further definition. Coordinated scans not specified. |
| TP-1 | Transport Physics | Steady-state plasma development |  |  | E | Closed 2006, Covered eslewhere |
| TP-2 | Transport Physics | Hybrid Regime development |  |  | E | See SSO proposals and reports. |
| TP-3.1 | Transport Physics | Determinetransport dependence on Ti/Te ratio in hybrid and steady-state scenario plasmas | G. Sips, C Greenfield, Takenaga, C Challis, | AUG, DIII-D, JET, JT-60U | D | Report for TP 3.0, new results, Define experimental conditions more carefully across machine. E.g. q95, beta, density, machine limitations |
| TP-3.2 | Transport Physics | Determine transport dependence on Ti/Te ratio in L-mode plasmas | V. Vershkov/N. Kirneva (T-10), A. Kraemer-Flecken/R. Jasper(TEXTOR), X. Duan (HL-2A), G. T. Hoang (TS) | T-10, TEXTOR, HL-2A, Tore-Supra, FTU(data mining) | E | Report for TP 3.0, new results |
| TP-4.1 | Transport Physics | Similarity experiments with off-axis ICRF-generated density peaking | J Stober, J Rice J. Ding | AUG, C-Mod, HT-7 | E | Closed 2006 |
| TP-4.2 | Transport Physics | Low momentum input operation effects on ExB shear and reduced transport | G. Sips/J. Stober (AUG), H. Takenaga (JT-60U), M. Wade (DIII-D), F. Crisanti (JET+FTU), O. Sauter (TCV), | JT-60U, JET, DIII-D, AUG, TCV | E | Report, new results |
| TP-4.3 | Transport Physics | Electron ITB similarity experiments with low momentum input | T. Donne (TEXTOR), K. Razumova (T-10), G. T. Hoang (TS), M. Romanelli(FTU),X.T.Ding(HL-2A),B.J.Ding(HT-7) | T-10, TEXTOR, Tore-Supra, FTU,HL-2A,HT-7 | E | Report, Moved to TP 8.4; Closed 2005 |
| TP-5 | Transport Physics | QH/QDB plasma studies | P. Gohil/L. Lao (DIII-D), N. Oyama/Y. Sakamoto (JT-60U), W. Suttrop(AUG) | DIII-D, JT-60U, JET, AUG | E | Report, new results |
| TP-6.1 | Transport Physics | Scaling of spontaneous rotation with no external momentum input | J. Rice (CMOD), J. deGrassie (DIII-D), F. Crisanti, L.G. Eriksson (JET-AUG-TS), Sakamoto (JT-60U), O. Sauter (TCV), C. Bush (NSTX), R. Jaspers (TEXTOR), H. Meyer (MAST) | CMOD, DIII-D, JET, JT-60U, TCV, MAST, NSTX, AUG, TEXTOR, Tore-Supra | E | Report, new results |
| TP-6.2 | Transport Physics | JT-60U/DIII-D Mach number scan similarity experiment | C. Petty/E. Doyle (DIII-D), Sakamoto/ M. Yoshida (JT-60U) | DIII-D, JT-60U | E | Report, preparation for 07, Linked to PEP 18 |
| TP-6.3 | Transport Physics | NBI-driven momentum transport study | M. Peng (NSTX), P. Gohil (DIII-D), Y. Sakamoto (JT-60U), M. Peng (NSTX), A. Field (MAST), G. Tardini (AUG), T. Tala(JET) | DIII-D, JT-60U, NSTX, MAST, AUG, JET | E | Report, preparation for 07, Machine commitments needed |
| TP-7 | Transport Physics | Measure ITG/TEM line splitting and compare to codes | F. Ryter/ C. Angioni/ G. Conway (AUG), J. DeBoo/R. Waltz/ E. Doyle (DIII-D), V. Vershkov/ D. Shelukhin/ S. Soldatov (T-10), A. Kraemer-Flecken (TEXTOR) | AUG, DIII-D, T-10, TEXTOR, JET | E | Report, new results |
| TP-8.1 | Transport Physics | NSTX/MAST ITB Similarity Experiments | M. Peng (NSTX), A. Field (MAST) | MAST, NSTX | E | Report, defer to 07, Waiting on PINI Upgrade on MAST |
| TP-8.2 | Transport Physics | Investigation of rational q effects on ITB formation and expansion | M. Austin (DIII-D), E. Joffrin (JET), K. Razumova(T-10), T. Donne (TEXTOR), D. Stutman(NSTX) | JET, DIII-D, T-10, TEXTOR,NSTX | E | Report, new results |
| TP-8.3 | Transport Physics | JT-60U/JET ITB Similarity Experiment | Y Sakamoto (JT-60U), P de Vries/X. Litaudon (JET) | JET, JT-60U | E | Report, defer to 07 |
| TP-8.4 | Transport Phsyics | T-10/TEXTOR/ HL-2A ITB Similarity Experiments | R. Jaspers (TEXTOR), K. Razumova (T-10), X. Duan (HL-2A), G. Giruzzi (TS) | T-10, TEXTOR, HL-2A, Tore-Supra | E | Report, will include HL-2A |
| TP-9 | Transport Phsyics | H-mode aspect ratio comparison | S. Kaye(NSTX), C. Petty (DIII-D), M. Valovic/A. Field (MAST) | NSTX, DIII-D, MAST | E | Report, new results |
| PEP-1+3 | Pedestal & Edge | Dimensionless identity experiments in JT-60U and JET: studies of ripple effects and rotation | G Saibene, V Parail, J Lonnroth and A Loarte (EFDA JET); N Oyama, H Urano, K Kamiya, K Shinohara (JAERI) | JET, JT-60U | E | Report, new results |
| PEP-2 | Pedestal & Edge | Pedestal gradients in dimensionally similar discharges and their dimensionless scaling | A. Loarte, M. Kempenaars, G. Saibene, M. Beurskens, (JET) T. Osborne, A.Leonard, M. Fenstermacher (DIII-D), L. Horton T. Eich, W. Suttrop, (AUG), J. Hughes(CMOD) | JET*, DIII-D, AUG, CMOD | E | Report, defer to 07 |
| PEP-4 | Pedestal & Edge | Stability analysis with improved edge treatment | L Lao, Y Kamada | AUG, DIII-D, JT-60U, MAST | P | Closed 2005 |
| PEP-5 | Pedestal & Edge | Dimensionless identity experiments with JT-60U type II ELMy H-modes in DIII-D | T Osborne, T Hatae | DIII-D, JT-60U |  | Closed 2005 |
| PEP-6 | Pedestal & Edge | Pedestal Structure and ELM stability in DN | H. Meyer(MAST), L. Horton (AUG), I. Nunes(JET), R. Maingi (NSTX) | AUG, MAST, NSTX, JET | E | Report, new results |
| PEP-7 | Pedestal & Edge | Pedestal width analysis by dimensionless edge identity experiments on JET, ASDEX Upgrade, Alcator C-Mod and DIII-D | G P Maddison*/ I Nunes† − JET (∗Euratom/UKAEA Fusion Association, †CFN/IST Lisbon), W. Suttrop, L. Horton (AUG), A Hubbard, J. Hughes (C-Mod), A. Leonard, T. Osborne, R. Groebner (DIII-D) | JET*, AUG, C-Mod, DIII-D | E | Report, new results |
| PEP-8 | Pedestal & Edge | Parameter similarity studies Quiescent H-mode regimes) | TBD | AUG, DIII-D, JET, JT-60U |  | Closed 2005 |
| PEP-9 | Pedestal and Edge | NSTX-MAST-DIII-D pedestal similarity | T Osborne, A Kirk, R Maingi | DIII-D, MAST, NSTX | E | Report, new results |
| PEP-10 | Pedestal and Edge | The radial efflux at the mid-plane and the structure of ELMs | Andrew Kirk, Albrecht Herrmann, J. Terry | AUG, MAST, CMOD | E | Report, new results |
| PEP-11 | Pedestal and Edge | Dimensionless comparison of L-H threshold and H-mode pedestals on C-Mod and ASDEX Upgrade | W Suttrop, F Ryter, A Hubbard | AUG, C-Mod | E | Closed 2005 |
| PEP-12 | Pedestal and Edge | Comparison between C-Mod EDA and JFT-2M HRS regimes | K. Kamiya, N. Oyama, (JAERI) and A. E. Hubbard | C-Mod, JFT-2M | E | Report; Closed 2005 |
| PEP-13 | Pedestal and Edge | Comparison of small ELM regimes in JT-60U and AUG and JET | N. Oyama, H. Urano (JT-60U), L.D. Horton/ W. Suttrop (AUG), G. Saibene, A. Loarte (EFDA-JET) | AUG, JT-60U, JET | E | Report, defer to 07 |
| PEP-14 | Pedestal and Edge | QH/QDB with Co/Counter Rotation Control IN JT-60U AND DIII-D | P. Gohil, L. Lao (DIII-D), N. Oyama, Y. Sakamoto (JT-60U) | DIII-D, JT-60U | E | Report; with TP-5, new results |
| PEP-15 |  | Testing influence of particle source on pedestal density profile | R Groebner, L D Horton | MAST, JT-60U | P | Closed 2005 |
| PEP-16 | Pedestal and Edge | C-MOD/NSTX/MAST SMALL ELM REGIME COMPARISON | A. Hubbard, R. Maingi, H. Meyer | NSTX, MAST, C-Mod | E | Report, preparation for 07, experiments to be attemted again |
| PEP-17 | Pedestal and Edge | Small ELM regimes at low pedestal collisionality | N. Oyama, Y. Kamada, H. Urano, K. Kamiya (JT-60U), T. Osborne, A. Leonard (DIII-D) | JT-60U, DIII-D, JET | E | Report, new results, Title needs changing. Grassy ELMs and low rotation, Titles to be changed and subnumbers used for 13, 16, and 17 |
| PEP-18 | Pedestal and Edge | Comparison of Rotation Effects on Type I ELMing H-mode in JT-60U and DIII-D | Y. Kamada (JT-60U), A. Leonard (DIII-D) | JT-60U, DIII-D | E | NEW, related to TP 6.2 |
| PEP-19 | Pedestal and Edge | Edge transport under the influence of resonant magnetic perturbations | T. Evans, M. Fenstermacher, R. Moyer, I. Joseph (DIII-D) B. Unterberg, H. Frerichs, D. Harting, M.W. Jakubowski, M. Lehnen, D. Reiter, O. Schmitz, D. Schega (TEXTOR), Liang(JET) | DIII-D, TEXTOR, JET | E | NEW |
| PEP-20 | Pedestal and Edge | Documentation of the edge pedestal in advanced scenarios | Pedestal: C. Maggi (AUG), R. Sartori (JET), R. Groebner (DIII-D), Y. Kamada/ N. Oyama(JT-60U) SSO TG: G. Sips (AUG), R. Sartori (JET), T. Luce (DIII-D), S. Ide /T. Suzuki (JT-60U) | JET*, DIII-D, AUG, JT-60U | E | NEW; with SSO-4, related to CDB-2 |
| DSOL-1 | Divertor & SOL | Scaling of Type I ELM energy loss | A. Loarte, M. Kempenaars, G. Saibene, M. Beurskens, A.Leonard, T. Osborne, M. Fenstermacher, T. Eich, W. Suttrop, L. Horton, J. Terry | JET, DIII-D, AUG Cmod, JT-60U | E | Report, defer to 07 |
| DSOL-2 | Divertor & SOL | Injection to quantify chemical erosion | TEXTOR (V. Phillips, S.Brezinsek), ASDEX-U ( R.Pugno, S.Brezinsek, A.Kallenbach), DIII-D (M. Fenstermacher, D.Whyte, A.McLean), JT-60 U (T. Nakano), JET (M.F. Stamp, S.Brezinsek,) | TEXTOR, JET, AUG, DIII-D, JT-60U | E | Report, new results |
| DSOL-3 | Divertor & SOL | Scaling of radial transport | Bruce Lipschultz, Tony Leonard, S. Lisgo, A. Kallenbach, N. Asakura | C-mod, ,MAST, DIII-D,JET, AUG, JT-60U | E | Report, new results |
| DSOL-4 | Divertor & SOL | Comparison of disruption energy balance in similar discharges and disruption heat flux profile characterisation | A. Loarte, G. Pautasso, P. Andrew, V. Riccardo, J. Paley, D. Whyte, R. Granetz, D. Humphreys, A. Kellman, and G. Counsell. | JET, DIII-D, AUG, MAST, C-mod, JT-60U | E | Report. Defer to 07 |
| DSOL-5 | Divertor & SOL | Role of Lyman absorption in the divertor | D Reiter (TEXTOR), J Terry(CMOD), S Lisgo(JET) | C-Mod, JET | E | Report came late C mod data obtained. Proposal to continue |
| DSOL-6 | Divertor & SOL | Parallel transport in the SOL | G Porter, B LaBombard, K Erents, N Asakura | DIII-D, JET, JT-60U, MAST and others | D | Report; Closed 2005 |
| DSOL-7 | Divertor & SOL | Multi-machine modeling and database for edge density and temperature profiles | Arne Kallenbach (AUG), G. Porter (DIII-D), A. Hubbard (C-Mod), N. Asakura (JT60-U), A. Kirk (MAST), W. Suttrop, L. Horton, T. Osborne, D. Coster , W. Fundamenski(JET) | Analysis, | P | Report; Closed 2005 |
| DSOL-8 | Divertor & SOL | ICRF Conditioning | Naoko Ashikawa (LHD), Jiansheng Hu (HT-7 and EAST), Volker Philipps (TEXTOR), Volker Rohde (ASDEX-Upgrade) | LHD, HT-7, EAST, TEXTOR, AUG | E | Report, preparation for 07 |
| DSOL-9 | Divertor & SOL | 13C injection experiments to understand C migration | Paul Coad, Peter Stangeby, Volker Philipps, Volker Rohde | JET, DIII-D, TEXTOR, AUG, JT-60U | E | Report, new results, DIII-D will do 9 if it does 12 |
| DSOL-10 | Divertor & SOL | Modeling of different gasses effects on disruption power deposition | D. Whyte (UW-Madison), M. Bakhtiari (JT-60U), K. Tsuzuki, Y. Kawano(JT-60U),P. Andrew (JET), Martin (TS), E. Tsitrone(TS),Matthews (JET), Hollmann (DIII-D) | JET, JT-60U, DIII-D, TS | P | No Report; Closed 2005 |
| DSOL-11 | Divertor & SOL | Disruption mitigation experiments | D. Whyte (MIT), T. Jernigan (ORNL), E. Hollmann (UCSD/DIII-D), Saint-Laurent (Tore Supra), V. Riccardo (JET), P. Andrew (JET), R. Granetz (MIT), K. Erents (JET), G. Matthews (JET), M. Lehnen (Juelich), G.Pautasso(AUG), B. Esposito (FTU) | DIII-D, Tore Supra, JET**, C-Mod, TEXTOR, AUG, JT-60U, FTU | E | Report, new results |
| DSOL-12 | Divertor & SOL | Oxygen wall cleaning | P. Stangeby, V. Phillips, J. Hu, J.Roth. | TEXTOR, HT-7, EAST, DIII-D, JET, AUG | E | Report, new results |
| DSOL-13 | Divertor & SOL | Deuterium codeposition with carbon in gaps of plasma facing components | K. Krieger, A. Litnovsky, K. Krieger, C. Wong,Ch. Brousset,B. Lipschultz, G. Counsell | AUG, TEXTOR, DIII-D, Tore-Supra, C-MOD, MAST, JT-60U, JET | E | Report, new results |
| DSOL-14 | Divertor & SOL | Multi-code, multi-machine edge modelling and code benchmarking | David Coster, Arne Kallenbach, Xavier Bonnin, Akiyoshi Hatayama, Hisato Kawashima, Tom Rognlien, Jim Strachan, Mathias Groth, Marco Wischmeier, D. Reiter | Codes only | P | Report, new results |
| DSOL-15 | Divertor & SOL | Inter-machine comparison of blob characteristics | J. Terry (C-Mod), G. Antar(PISCES), N. Asakura (JT-60U), J. Boedo/D. Rudakov (DIII-D), J. Egedal (VTF), W. Fundamenski and V. Naulin (JET), O. Grulke (IPP-Griefswald), Albrecht Herrmann (AUG), C. Hidalgo (JET and TJ-II), R. Maqueda/S. Zweben (NSTX), Y. Xu (TEXTOR) , P. Ghedrih (TS), A. Kirk (MAST), G. Xu(HT-7) | C-Mod, PISCES, TEXTOR, VTF, NSTX, TJ-II,JET, TCV, HT-7, Tore-Supra, AUG, JT-60U, MAST, FTU | P | Report, new results |
| DSOL-16 | Divertor & SOL | Determination of the poloidal fueling profile | Mathias Groth, Gary Porter, Anthony Leonard, Arne Kallenbach, David Coster, W. Fundamenski, Marco Wischmeier, Steve Lisgo, David Elder, N. Asakura | DIII-D, AUG, JT-60U, MAST, JET | D | Report, new results |
| DSOL-17 | Divertor & SOL | Cross-machine comparisons of pulse-by-pulse deposition | C. Skinner, V. Rohde, A. Kreter (TEXTOR-JET) | NSTX, AUG, JET, TEXTOR | E | Report, new proposal made |
| DSOL-19 | Divertor & SOL | Impurity generation mechanism and transport during ELMs for comparable ELMs across devices | A. Loarte, W. Fundamenski, R. Pitts, M. Fenstermacher, M. Groth, A. Herrmann, V. Rohde, D. Whyte, T. Nakano and G. Counsell, V. Soukhanovski(NSTX) | AUG, JET, DIII-D, C-mod, JT-60U, MAST,NSTX |  | NEW |
| MDC-1 | MHD, Disruptions & Control | Disruption mitigation by massive gas jets See DSOL-11 | D. Whyte (MIT), T. Jernigan (ORNL), E. Hollmann (UCSD/DIII-D), M. Bakhtiari (JT60-U), F. Saint-Laurent (Tore Supra), V. Riccardo (JET), P. Andrew (JET), R. Granetz (MIT), K. Erents (JET), G. Matthews (JET), M. Lehnen (Juelich), G. Pautasso (AUG) | DIII-D, Tore Supra, JET**, C-Mod, TEXTOR, AUG | E | See DSOL-11 report |
| MDC-2 | MHD, Disruptions & Control | Joint experiments on resistive wall mode physics | H Reimerdes, A Garofalo (DIII-D), , S D Pinches (JET), R Koslowski (TEXTOR), Matsunaga (JT-60U), S Sabbagh (NSTX), H Zohm (AUG), M Gryaznevich (MAST),Y Liu (MARS-F code) | DIII-D, JET, NSTX, JT-60U, MAST, AUG, TEXTOR | D | Report, new results, Split into 2.1 and 2.2? And updates |
| MDC-3 | MHD, Disruptions & Control | Joint experiments on neoclassical tearing modes (including error field effects) | R Granetz (C-Mod), R Buttery(JET), M Maraschek (JET), M Maraschek (AUG), R La Haye (DIII-D) | C-mod, JET, AUG, DIII-D | E | Report, new results |
| MDC-4 | MHD, Disruptions & Control | Neoclassical tearing mode physics - aspect ratio comparison | M Maraschek (AUG), D Howell (MAST), E. Frederickson(NSTX), R. LaHaye(DIII-D) | AUG, MAST, NSTX, DIII-D | E | Report. Defer to 07 |
| MDC-5 | MHD, Disruptions & Control | Comparison of sawtooth control methods for neoclassical tearing mode suppression | O. Sauter, R Pinsker, R La Haye (DIII-D), H. Zohm (AUG), S. Coda(JET), R Buttery (JET), ,J Menard (NSTX), T Goodman (TCV), Yi Liu (HL2A), S Wukitch(C-mod),F. Gandini(FTU), A. Isayama (JT-60U) | AUG , DIII-D, JET, NSTX, TCV, HL2A, Cmod, FTU, JT-60U | E | Report, new results |
| MDC-6 | MHD, Disruptions & Control | Low beta error field experiments | S Wolfe, I Hutchinson (C-Mod), T Hender(JET), M. Schaffer (DIII-D), T. Scoville (DIII-D), R Koslowski (TEXTOR), D Howell (MAST), Menard (NSTX) | C-mod, TEXTOR, MAST, DIII-D, NSTX, JET(done) | E | Report; closed 2006, work finished |
| MDC-7 | MHD, Disruptions & Control | Improving NTM modelling/ extrapolation to ITER | H Zohm and others | AUG, DIII-D, JET, JT-60U, MAST | P | Report; Closed 2005 |
| MDC-8 | MHD, Disruptions & Control | Current drive prevention/stabilisation of NTMs | Buttery (JET), A. Isayama (JT60-U), Maraschek, Zohm (AUG), La Haye (DIII-D), Cirant(FTU), S. Wolfe | JET, AUG, JT-60U, DIII-D, FTU, Cmod, NSTX, TEXTOR | E | Report, new results |
| MDC-9 | MHD, Disruptions & Control | Fast ion redistribution by beam driven Alfvén modes and excitation threshold for Alfvén cascades | A.Fasoli, D.Borba(JET/AUG), S.Pinches and D.Testa (JET), K. Shinohara (JT60-U), W.Heidbrink (DIII-D),R. Nazikian(DIII-D) E. Frederickson(NSTX), M. Gryaznevich/S. Sharapov(MAST), P. Martin (AUG) | JT-60U, JET, DIII-D, NSTX, MAST, AUG | E | Report; new results, closed 2006 with opening of MDC-11 |
| MDC-10 | MHD, Disruptions & Control | Measurement of damping rate of intermediate toroidal mode number Alfvén Eigenmodes | A.Fasoli / A. Klein(JET)/ D.Testa (TCV/ JET), J.Snipes (C-Mod), M. Gryaznevich/(MAST), N. Gorelenkov (NSTX) | JET, C-Mod, MAST, NSTX | E | Report, new results and preparation for 07 |
| MDC-11 | MHD, Disruptions & Control | Fast ion losses and Redistribution from Localized Aes | D Borba (JET), M.Gryaznevich (MAST), R Nazikan, B Heidbrink (DIII-D), Shinohara (JT-60U), E Fredrickson (NSTX), H. Zohm (AUG) | JET, DIII-D, JT-60U, NSTX, MAST, AUG | E | NEW |
| MDC-12 | MHD, Disruptions & Control | Non-resonant Magnetic Braking | S Wolfe (C-Mod), T Hender (JET), D Howell, M Gryaznevich (MAST), R La Haye (DIII-D), R Koslowski (Textor), S. Sabbagh (NSTX) | JET, DIII-D, C-Mod, NSTX, TEXTOR, MAST | E | NEW |
| SSO-1.1 | Steady-State Operation | Document performance boundaries for steady state target q-profile | C. Challis (JET), G. Sips (AUG), T. Luce (DIII-D), Y. Sakamoto (JT-60U), P. Bonoli (CMOD) | JET, AUG, DIII-D, JT-60U, C-mod | E | Report, new results |
| SSO-1.2 | Steady-State Operation | Qualify other q-profiles for steady state operation | S. Ide, C. Greenfield (DIII-D), X.Litaudon,B.J.Ding(HT-7) | JT-60U, JET, HT-7,DIII-D, C-mod | E | Report; dropped for 2007 |
| SSO-1.3 | Steady-State Operation | Control of high bootstrap plasmas | P. Politzer, D. Moreau(JET), V. Basiuk(TS), S. Ide(JT-60U), O. Sauter (TCV), G. Sips | DIII-D, JET, Tore-Supra, JT-60U, TCV, AUG |  | Report; JT-60U results, defer to 2008-2009 |
| SSO-2.1 | Steady-State Operation | Qualifying hybrid scenario at ITER-relevant parameters | E. Joffrin(JET), S. Ide(JT-60U),T. Luce (DIII-D), G. Sips (AUG), A. Hubbard (CMOD) | JET, JT-60U, DIII-D, AUG, C-mod | E | Report; New area, extended from completed SSO-2.1 in 2006 |
| SSO-2.2 | Steady-State Operation | MHD in hybrid scenarios and effects on q-profile | S. Günter (AUG), S. Pinches (JET), P. Politzer (DIII-D), Isayama (JT-60U), C. Kessel (NSTX), A. Hubbard (CMOD) | AUG, JET, DIII-D, JT-60U, NSTX, C-mod | E | Report, new results |
| SSO-2.3 | Steady-State Operation | ρ* dependence on confinement and stability in hybrid scenarios | C. Petty (DIII-D), D. McDonald (JET), J. Stober (AUG), S. Ide (JT-60U), A. Hubbard (CMOD) | DIII-D, JET, AUG, JT-60U, C-mod, NSTX | D | Report, preparation for 07 |
| SSO-3 | Steady-State Operation | Modulation of actuators to qualify real-time profile control methods for hybrid and steady state scenarios | D. Moreau(JET), E.Joffrin(JET),D. Mazon(TS), A. Sips,(AUG), J. Ferron (DIII-D), T. Suzuki(JT-60U), X.D.Zhang(HT-7), P. Bonoli (C-Mod) | JET, Tore-Supra, AUG, DIII-D, JT-60U, HT-7, C-mod | D | Report - New name (previously "Real time q-profile control in hybrid and teady state scenarios), A specific proposal identifying the particular plasma scenario and reference pulses should be defined in the proposal. |
| SSO-4 | Steady-State Operation | Documentation of the edge pedestal in advanced scenarios | Pedestal TG: C. Maggi (AUG), R. Sartori (JET), R. Groebner (DIII-D), Y. Kamada (JT-60U), N. Oyama (JT-60U) SSO TG: G. Sips (AUG), R. Sartori (JET), T. Luce (DIII-D), S. Ide/T. Suzuki (JT-60U) | AUG, JET* , DIII-D, JT-60U | E | Report; with PEP-20, NEW |
| SSO-5 | Steady-State Operation | Simulation and validation of ITER startup to achieve advanced scenarios | E. Joffrin (JET), G. Sips (AUG), T. Luce (DIII-D), S. Ide (JT-60U), B. Lipschultz (C-Mod), X. Gong (EAST), G. Giruzzi (Tore Supra) | JET, DIII-D, AUG, JT-60U, C-Mod, EAST, Tore Supra | E | NEW |
| SSO-6 | Steady-State Operation | Ability to obtain and predict off-axis NBCD | C. Challis (JET) (?), S. Günter (AUG) (?), T. Luce (DIII-D) (?), T. Suzuki (JT-60U), R. Akers (MAST) (?) | JET, DIII-D, AUG, JT-60U, MAST | E | NEW |
| DIAG-1 | Diagnostics | Assessment of the effect of noise on vertical velocity measurement | Tim Hender (JET), Y Kamada (tbc) (JT-60U), G Navratil (DIII-D), D. Gates (NSTX), J. M. Moret (TCV) | JET, JT-60U, TCV, NSTX, AUG, C-mod | P | No Report; no proposal from group, CLOSED |
| DIAG-2 | Diagnostics | First mirror Qualification | K. Vukovov, A. Litnovsky, M. Rubel, D. Rudakov, G. DeTemmerman, V. Voitsenya, N. Ashikawa, S. Masuzaki, A. Sagara, A. Herrmann, V. Rohde, V. Zhou(HL-2A), V. Kumar (Aditya), S. Pandya, C.Skinner(NSTX) | T-10, TEXTOR, LHD, JET, DIII-D, TCV, AUG, LHD, HL-2A, Aditya, NSTX, HT-7, Tore-Supra | E | Report; new results |
|  |  |  |  | * subject to HRTS availability | E = Well defined, accepted joint experiment. |
|  |  |  |  | ** subject to DMV availability | D = Needs further definition |
|  |  |  |  |  | P = Programmatic activity, not joint experiment |